## Slide 1: SysML in META
Greg Eakman, Ph.D.
BAE Systems
V 1.2
7/7/2011

## Slide 2: SysML in META
Model-driven systems engineering
* Capture of vehicle Reference Architecture
Capture of requirements and mapping to abstract architecture
  * Map requirements onto components and attributes
  Use of parametrics-like capability to define constraints for component selection
  * Domain specific language based on SysML
* Front end to AMIL – transform SysML elements to AMIL
Definition of CML meta model and CML contents
  Use SysML to generate CML schema
Framework for test case design, automated test case generation
  Model environmental components
Feedback to user
  Display of component PCCs within Reference Architecture views
  Show selections from CML
* Target for July demo

## Slide 3: Vehicle Reference Architecture
Model the invariants of ground vehicles
No need to start from scratch for every new vehicle
Account for commonalities, variabilities (product line concepts)
Map requirements onto architecture
Captures relationships from all viewpoints
With behavioral component models, requirements become executable
Use as a framework for early requirements analysis
  Identified as key time sink as customer may change mind, or does not understand conflicting or unfeasible requirements.
Thermodynamic
view
Power view

## Slide 4: Reference Architecture Data Partitions
Vehicle reference architecture
  Invariant model of a generic ground vehicle
Instance specific requirements and constraints
  Vehicle specific that drive choices within the framework of the architecture
Component Model Library (CML)
  Abstract components
  Detailed component info from all viewpoints
    Operational limits, parameters, interfaces, behaviors
    Equations and executable models that can plug into a hybrid, distributed, simulation framework like HLA.
Integration patterns: Patterns for connecting components
    Eg. Brake pedal to brakes
      Hydraulics
      Electrical sensor on pedal, networked to actuator on brakes
AMIL Output – component selections and interconnections

## Slide 6: Vehicle Chassis Reference Architecture

## Slide 7: EntryWay Reference Architecture*
* Images used without permission

## Slide 8: Analysis of Alternatives (AoA)
META should support the AoA for components
All requirements flow to each alternative
A component may have many alternatives
AMIL and its components, and simulations and results, help select best alternative
EntryWay1: Hatch
orientation: az=0, el=90
opening.area=5.25 sq ft
EntryWay2: Door
orientation: az=90, el=0
opening.area=15 sq ft

## Slide 9: AoA (2)
AutoSelect

## Slide 10: Component and Interfaces
Components have interfaces in multiple viewpoints
  Eg. Power, therodynamic, mechanical, structural, …
All viewpoints must eventually be accounted for
  Many may be defaulted/ignored during early design stages
Interfaces (SysML ports) define connection/interaction points
  With other components of the system
  With the environment
Connection with CML

## Slide 11: Domain Specific Language for Vehicle Requirements
Define new component types
  Attributes
  Interfaces
Insert components into architecture
Attributes optionally filled in, or unspecified
Interfaces connected or free
Connection patterns
New viewpoints
Components viewed on multiple diagrams
Connect new component types with CML

## Slide 12: Modeling with the RA
The Reference Architecture is a starting place for defining a component
  Describes all the possible configurations
  Modeling documents the requirements and design choices to select one configuration of components
RA defines a meta-model for a component
The model defines a specific configuration of block instances, links, and properties

## Slide 13: Mapping Requirements to the RA
General requirements are mapped to reference architecture meta-model components. Eg. Safety requirements
Specific requirements are mapped to block instances in the model
The effects of requirements on block properties are captured in a dialog

## Slide 14: Modeling with the RA
Sometimes the model becomes normative
  expressing the requirement directly
The ramp motor shall have two operating switches,
one by the driver and one in the cargo bay

## Slide 15: META Reference Architecture Meta-model
Architectural model consists of
  Components
  Attributes
  Interfaces
Create ground vehicle requirements domain specific language based on SysML

## Slide 16: SysML for Test Case Design Framework
Quantitative
Qualitative
Selection of system and environmental components and input parameter models

## Slide 17: Quantitative Simulation Environment
Cannot remove quantitative, monte carlo sims from process
  Can use it more efficiently with input from qualitative sim
Distributed, cloud-based
Component behaviors “plug-in” to simulation bus
Scalable
  Hardware in the loop
  Human in the loop
  Training
Existing frameworks already exist, eg. HLA
Environmental components are just like system components

## Slide 18: Relation of Qualitative and Quantitative Simulation
Qualitative sim finds possible reachable states of a component
  Some may not be reachable in the system due to input bindings
Use quantitative to verify qualitative results
Fault injection
  Initialize component into bad state identified by qualitative simulation
  Determine how the rest of the system responds
  Needed because qualitative simulations are not composable, and defect subcomponent states may be omitted from higher level simulations

## Slide 19: Ground Vehicle Viewpoints

## Slide 20: Reference Architecture Meta Model

## Slide 22: Requirements and Test Cases

## Slide 23: Semantic Linking Enables Agile Design, Test, and Diagnosis
Semantic linkage enables:
Thorough exploration of design alternatives with existing design tools
Distributed design efforts and crowd sourcing of design alternatives
Use of New algorithms (qualitative simulation and reach set analysis) for stress testing and diagnosis revealing design tradeoffs;
    (On exemplary COA Planning Problem: 1015 (est.) run-time compression for the same analysis as compared to traditional stochastic simulator (e.g., OneSAF)
Discover & Diagnose Issues Resulting from Design Choices (and Req’ts) Early
Software Infrastructure
Goal Capability
1
2
3
4
5
Implements
3
Master Model
Qualitative Model
Quantitative Model
Reach Set Analysis
Envisioner
Galileo Simulation Compiler
Simulation Environment
AMIL Service
Design Modeling Tools
MagicDraw
Pro/E
MatLab
Plug-ins / Wrappers
Component Model Library
1
5
2
4
SysML Model /
Use Cases
Pro/E Model
MatLab Model
Inform
Design

## Slide 24: A Systemic Solution to Achieve 5x Reduction In Development Time
Confidently ID & Eliminate Design Failures in Virtual Environment Before Production
ARRoW (Adaptive, Reflexive, Robust Workflow)
Early and Continuous
Testing, Verification, and Validation
Do in Parallel Currently Serial Design Steps
  Across design elements
  Across levels of abstraction
Integrate Existing Design Tools
  Detect unwanted interactions “at the seams” early when costs can be minimized
Avoid Problems from “Leaky Abstractions” via Design Lookaheads
Reveal Important Design Tradeoffs Early
  Metrics for Complexity and Adaptability
  Algorithms Facilitating Stress Testing of Designs

## Slide 25: System of Systems!
25
090112
jring@amug.org
25
Notes: 25
25
Or, you can use the System of Systems Systems Engineering process propounded by U.S. Dept. of Defense.