## Slide 1: Scale-Space Representations and their Applications to 3D Matching of Solid Models
Dmitriy Bespalov† Ali Shokoufandeh†
William C. Regli†‡ Wei Sun‡
Department of Computer Science†
Department of Mechanical Engineering & Mechanics‡
College of Engineering
Drexel University
3141 Chestnut Street
Philadelphia, PA 19104

## Slide 2: Goals
Flexible content-based, feature-based and shape-based retrieval of CAD data
  Manage large-scale engineering databases
Propose a unified approach to 3D model matching based on ideas spanning
  Computer Vision & Pattern Recognition
  Computer Aided Design & Solid Modeling
  Computer Graphics & Computational Geometry
Integrate and test new algorithms with the National Design Repository (http://www.designrepository.org)

## Slide 3: Selected Related Work
Comparing Solid Models (SM & Engineering community)
  Feature relationship graphs [Elinson et al. 97; Cicirello and Regli 99,00,01,02]
  Automatic detection of part families [Ramesh et al 00]
  Topological similarity assessment [Sun et al 95; McWherter et al 01,02]
Comparing Shape Models (Graphics community)
  Multi-resolutional Reeb Graphs [Hilaga et al., 01]
  Shape distributions [Osada, Funkhouser et al, 01,02,03]; [Ip et al 02,03]
  2D views of 3D objects [Cyr and Kimia, 01]
Hierarchical graph matching (Computer Vision community)
  [Shokoufandeh et al 99], coarse-to-fine bipartite matching to multi-scale blobs;
  [Siddiqi et al 99], spectral graph characterization for matching of shock graphs;
  [Pelillo et al 99] hierarchical matching as a maximum clique problem;
  [Shokoufandeh et al 02] combined spectral and geometric neighborhood information to match multi-scale blob and ridge decompositions
Other Related Work
  [Lamdan/Wolfson 88]; S3 [Berchtold et al SIGMOD 97]; [Smith et al IEEEToNN 97]; [Elber et al 97,99,01]; 3DBase [Cybenko et al 96,97]; [Szykman et al 99,00,01];

## Slide 4: Traditional CAD Representation
Watertight boundary-representation solid
  Implicit surfaces
  Analytic surfaces
  NURBS, etc
Topologically and geometrically consistent
Produced by kernel modelers and CAD systems

## Slide 5: Traditional Shape Representation
Usually a mesh or point cloud
Usually an approximate representation
No explicit in/out
Sometimes error prone
  STL files, acquired data
Produced by CAD systems, animation tools, laser scanners, etc

## Slide 6: Our Previous Work
Implemented Reeb Graph based matching technique introduced by [Hilaga et al., 01]
Reeb graph: an object skeleton determined using continuous scalar function µ defined on object
  Mathematical basis in Morse theory
Reeb graph representations
  Are invariant to translation and rotation
  Can be multi-resolutional, i.e. hierarchical, for faster matching of objects and classes

## Slide 7: Multiresolutional Reeb Graphs for the models

## Slide 8: Summary of the Experiments
There are often false-positives and non-similar models
Changes in topology affect performance
Only significant shape deformations affect performance
Can classify groups with homogeneous topology
Is sensitive to quality of mesh refinement
Non-similar model
False-positives
~
=
not similar
~
=
not similar
~
=
not similar

## Slide 9: What is a Scale Space Representation?
Commonly used for Coarse-to-Fine representations of an object
Very popular in computer Vision
  Constructed via spatial filters: Gaussian pyramids, Wavelets…
Basic Idea:
  At each scale, topologically relevant components will decompose the object into so called salient parts
  Recursive application of this paradigm will create the object’s scale space hierarchy

## Slide 10: Why Scale Space Representation?
A unified framework for matching
Different features can be parameterized as different scale space decompositions
  design, manufacturing, topology or shape features
Robust & consistent across noisy and diverse data sets

## Slide 11: Approach to Scale Space Matching of Solid Models
Start with CAD model
  Obtain polyhedral representation
Perform geometry-based decomposition
  Obtain a segmentation into “features”
Construct hierarchical “feature” graph
  Singular value decomposition
Use hierarchical matching to compare graphs

## Slide 12: Side Note: Compare Features Scale Space CAD/CAM

## Slide 13: Algorithm Overview (I)
Given model P, compute mesh representation M
Define measurement function: Our d is shortest path (approx) between every two points on M will be captured in a pair-wise distance matrix D.
(similar to approximation of geodesic distance measure used by Hilaga in SIGGRAPH 2001)
d(p1,p2)

## Slide 14: Algorithm Overview (II)
3. Decompose M into components relevant using a singular value decomposition of distance matrix D Note: this creates a clustering based on the angle between a vector Opi and the basis vectors (ck, ck-1)

## Slide 15: Algorithm Overview (III)
4. Recursive feature decomposition using two principle components creates binary feature trees
feature tree for swivel
feature tree for simple_bracket

## Slide 16: Algorithm Overview (IV)
5. Compare feature trees (bottom up dynamic programming) using sub-tree edit distances
6. Calculate model similarity based on an overall similarity of matched components
swivel
simple_bracket

## Slide 17: Algorithmic Complexity
Bisection process:
  SVD decomposition takes O(n3).
  Polyhedral representation creates a planar graph (2D manifold); if only neighboring vertices are used in construction of the distance matrix, SVD decomposition is faster and takes O(n2).
Graph matching:
  n1 & n2 are the number of nodes in the graphs; b is the branching factor (e.g. 2)

## Slide 18: Experiments
Measured “technique’s performance”:
  Ability of technique to distinguish between human-defined categories
Used distance matrix for illustration of experimental results
Models in the dataset
Similarity value between two models
Darker regions correspond to higher similarity values
Models grouped together
Desirable result

## Slide 19: Empirical Results
Dataset of 40 CAD models from different 10 classes
Classification based on engineering rules, not specifically their shapes

## Slide 20: Scale Space Distance Matrix
Note: Darker color represents higher similarity.

## Slide 21: Controlling Feature Decomposition: When to Stop?
Idea: automate by assigning a measurement, f, to assess the “quality” of each bisection
Given:
d(u,v): the distance between points u and v on the model’s surface
M: the original model’s point set E: edges connecting points in M M1: an existing component of M
Then:
Where: Inter-component coherence
Cross-component coherence
Note: f measures the coherence of a component relative to a potential decomposition.

## Slide 22: For Example: Bisection (b=2)
In the case of bisection, compute f(M1) with respect to decomposition of M1 into M2 and M3
Idea: bisect M1 into M2 and M3 if and only if the resulting coherence is better than that of M1 alone: f(M1) < 0.5

## Slide 23: Example Decomposition
Fork.sat

## Slide 24: Example Decomposition
Fork.sat

## Slide 25: Example Decomposition
Fork.sat

## Slide 26: Example Decomposition
Fork.sat

## Slide 27: Example Decomposition
Fork.sat

## Slide 28: Example Decomposition
No notch
A small notch
Fork.sat

## Slide 29: Side Note: Compare Features Scale Space CAD/CAM

## Slide 30: Summary
Research Contributions
  A scale-space approach to matching CAD models
    Bridging “CAD Features” and “Computer Vision Features”
  A general framework for CAD indexing
  Empirical validation/assessment of the technique
Future Work
  Use Scale-Space representation to index and retrieve solid models in the database
  Integrate this approach into the National Design Repository: from 40 parts to 40,000 parts!

## Slide 31: Q&A
For more information http://gicl.cs.drexel.edu http://aal.cs.drexel.edu http://www.designrepository.org
Sponsored (in part) by: ONR Grant N00014-01-1-0618 NSF ITR/DMI-0219176 NSF CAREER Award CISE/IIS-9733545