## Slide 1: A Stochastic Graph Grammar Algorithm for Interactive Search
Rahul Rai
Assistant Professor
Department of Mechanical Engineering
California State University at Fresno
Fresno, California 93740
rarai@csufresno.edu
Matthew I. Campbell
Associate Professor
Automated Design Laboratory
Department of Mechanical Engineering
University of Texas at Austin
Austin, Texas 78712-0292
mc1@mail.utexas.edu
Tolga Kurtoglu
Research Scientist
Mission Critical Technologies
Intelligent Systems Division
NASA Ames Research Center
Moffett Field, California 94035
tolga.kurtoglu@nasa.gov

## Slide 2: Introduction
generative grammars is a powerful approach to represent different topologies, configurations or shapes within a single search space
  approaches the representational capacity of human designers that create and compare wildly different solutions during the conceptual design phase
  We are interested in how grammars can be used to interactively guide human designers or even automatically find promising concepts
grammars merely define a space or tree of solutions
  not a means to search this space
  search trees -- intractably large set of solutions
  Need some way to evaluate concepts
    target specific areas of the tree that best meet the designer’s expectations.
Evaluation completely left to humans
  Difficult on concepts when no dimensions are provided

## Slide 3: Approach
present a sample of solutions to the designer
Get feedback
use that information to find better solutions in the search tree
seeks solutions to maximize the designer’s preference
reflecting the user input onto the generative grammar rules
  which rule
  combination of rules
  ordering of rules
  time to execute a particular rule
…leads to the best design

## Slide 4: Seed Rules for necktie knot grammar
In order to begin any tie knot a triangular basis has to be created. This beginning move creates three regions L C R (Left, Center, Right). This gives rise to seed rules. One can begin in two way Li and Lo (i denotes in plane and o denotes out plane).

## Slide 5: Continuing rules for tie knot
One can continue from the seed rule by implementing one of the six rules shown here
There are two restriction on continuing rules.
First, the i and o has to alternate
Second, next step cannot have same basis, i.e., if previous step is L then next step has to be either C or R.

## Slide 6: Terminating rules for tie knots
A tie knot can only terminate in one of the possible two ways shown above.
T denotes (termination and no more rules can be applied)

## Slide 7
18 graph grammar rules for tie knots
Based on initiation, continuing, and terminating aspects of tie knot, only 18 graph grammar rules can be deduced for the tie knot problem. The rules code in graphsynth are as follows:
Rule 1
LHS Lo
RHS LoCi
Rule 2
LHS Lo
RHS LoRi
Rule 4
LHS Ri
RHS RiLo
Rule 3
LHS Ri
RHS RiCo
Rule 5
LHS Co
RHS CoLi
Rule 6
LHS Co
RHS CoRi

## Slide 8
Rule 11
LHS Li
RHS LiCo
Rule 12
LHS Li
RHS LiRo
Rule 14
LHS Ro
RHS RoLi
Rule 13
LHS Ro
RHS RoCi
Rule 16
LHS Ci
RHS CiLo
Rule 15
LHS Ci
RHS CiRo
Rule 18 (Initiation )
LHS Null
RHS Lo
Rule 17 (Initiation )
LHS Null
RHS Li
Rule 19 (Termination )
LHS Co
RHS CoT
Rule 7
Rule 8
Rule 9
Rule 10
Rule 11
Rule 12
Rule 13
Rule 14
Rule 15

## Slide 9
Four in hand knot
Li
Seed graph (Null)
Step 1
Applicable Rules 13, 14
Li
Applicable Rules 7, 8
Step 2
Vertex where to apply a rule in the LHS of a step
4
Li
Li
Ro
Co
T
Applicable Rules 9, 10
Step 3
Li
Ro
Li
Ro
Li
Applicable Rules 7, 8
Step 4
Li
Ro
Li
Li
Ro
Co
Li
Applicable Rules 5, 6, 15
Step 5
Li
Ro
Li
Li
Ro
Co
A green number denote that rule selected for application among applicable rules

## Slide 10
Cross knot 1
Li
Seed graph (Null)
Step 1
Applicable Rules 13, 14
Vertex where to apply a rule in the LHS of a step
4
Ro
A green number denote that rule selected for application among applicable rules
Li
Step 2
Applicable Rules 7,8
Li
Ro
Li
Ro
Step 3
Applicable Rules 9, 10
Li
Ci
Ro
Step 4
Applicable Rules 11,12
Li
Ci
Ro
Li
Ci
Ro
Step 5
Applicable Rules 9,10
Ro
Li
Ci
Ro
Ro
Li
Ci
Ro
Li

## Slide 11
Li
Ro
Co
T
Li
Ci
Ro
Cross knot 2
Applicable Rules 7,8
Ro
Li
Ci
Ro
Li
Ro
Li
Ci
Ro
Li
Co
Step 6
Co
Ro
Li
Ci
Ro
Li
Applicable Rules 5, 6, 15
Step 7

## Slide 12
Windsor 1
Li
Seed graph (Null)
Step 1
Vertex where to apply a rule in the LHS of a step
4
Li
Step 2
Li
Co
Li
Co
Step 3
Applicable Rules 5, 6, 15
Li
Li
Co
Step 4
Li
Li
Co
Step 2 and 3
Li
Li
Co
Ro
Li
Li
Co
Ro
Applicable Rules 9,10
Li
Li
Co
Ro
Ci
Step 5
A green number denote that rule selected for application among applicable rules
Applicable Rules 13, 14
Applicable Rules 7,8
Applicable Rules 7,8

## Slide 13
Li
Ro
Co
T
Ci
Applicable Rules 11, 12
Windsor 2
Li
Li
Co
Ro
Ci
Li
Li
Co
Ro
Step 6
Ro
Ci
Applicable Rules 9, 10
Li
Li
Co
Ro
Step 7
Ro
Ci
Li
Li
Co
Ro
Li
Ro
Ci
Applicable Rules 7,8
Li
Li
Co
Ro
Step 8
Li
Ro
Ci
Li
Li
Co
Ro
Co
Li
Ro
Ci
Applicable Rules 5,6,15
Li
Li
Co
Ro
Step 9
Co
Li
Ro
Ci
Li
Li
Co
Ro

## Slide 14
Small knot
Seed graph (Null)
Step 1
Vertex where to apply a rule in the LHS of a step
4
A green number denote that rule selected for application among applicable rules
Lo
Co
Ri
T
Applicable Rules 13, 14
Step 2
Lo
Applicable Rules 1, 2
Lo
Ri
Step 3
Applicable Rules 3, 4
Lo
Ri
Lo
Co
Ri
Step 4
Applicable Rules 5 ,4, 15
Lo
Co
Ri
Lo

## Slide 15: Maximum of Nine Steps (85 solutions)
Lo
Ri
Ci
Lo
Lo
Co
Ro
Ci
Ci
Ri
Ci
Li
Ri
Li
Ri
Lo
Ro
Ro
Co
Lo
Co
Ro
Co
Lo
Co
Lo
Ro
Lo
Ro
Lo
Co
Ci
Li
Ri
Ci
Ri
Li
Ri
Ci
Ri
Li
Ci
Li
Ci
Li
Ri
Ri
Ci
Li
Ri
Li
Ci
Li
Ri
Ci
Ri
Li
Ri
Ci
Ri
Li
Ci
Ro
Lo
Co
Lo
Co
Ro
Lo
Ro
Lo
Co
Lo
Ro
Lo
Ro
Lo
Ro
Co
Ro
Lo
Ro
Ro
Lo
Co
Lo
Co
Ro
Lo
Ro
Co
Ro
Lo
Ro
Co
Lo
Co
Lo
Ro
Lo
Ro
Lo
Co
Ro
Lo
Ro
Lo
Ro
Co
Lo
Co
Ro
T1
T2
T3
T
T5
T6
T7
T8
T16
T9
T24
T23
T10
T11
T4
T12
T13
T14
T15
Ri
Co
Li
Co
T17
Ri
Co
T22
Li
Co
T19
Li
Co
Ri
Co
Ri
Co
Li
Co
T25
Ri
Co
T26
Ri
Co
T27
Li
T29
T28
Co
Li
Co
T20
Ri
Co
T30
Ri
Co
T31
Ri
Co
T32
Li
Co
T33
Ri
Co
T34
Ri
Co
T35
Li
Co
T36
Li
Co
T37
Ri
Co
T38
Ri
Co
T39
Li
Co
T40
Li
Co
T41
Li
Co
T42
Li
Co
T43
Ri
Co
T44
Li
Co
T45
Li
Co
T46
Ri
Co
T47
Ri
Co
T48
Li
Co
T49
Ri
Co
T50
Li
Co
T51
Ri
Co
T52
Ri
Co
T53
Ri
Co
T54
Li
Co
T55
Ci
Ci
Li
Co
T57
Lo
Ri
Co
T58

## Slide 16: title: “A Stochastic Graph Grammar Algorithm for Interactive Search”
the tree is never explicitly represented
  large and difficult to visualize
  may easily contain more states than the computer can store
  1010 =9.3 TB if each state in only one kilobyte
However, the number of rules that lead to these solutions is often a small and manageable size
  grammar rules represent heuristics or constraints provided by experts in the particular design domain
grammar rules make definitive changes to a particular concept and their use is often clearly discernible within the final candidate solution
  makes sense to gather statistics on the rules used to navigate the search tree
In the necktie grammar, rules define shape and size of the knot.

## Slide 17: Stochastic Process
any given state in the tree, a set of options is determined
rule3
rule1
rule6
rule7
Database |  | 
rule | Fitness (higher is better) | Popularity (lower is better)
1 | 1.2 | 5
2 | -0.4 | 3
3 | 0.8 | 2
4 | 2.5 | 2
5 | -1.6 | 7
6 | N/A | 0
7 | -1.3 | 6

## Slide 18
rule3
rule1
rule6
rule7
rule | Fitness (higher is better) | Popularity (lower is better)
1 | 1.2 | 5
2 | -0.4 | 3
3 | 0.8 | 2
4 | 2.5 | 2
5 | -1.6 | 7
6 | N/A | 0
7 | -1.3 | 6
 | Fit. | Pop. | f1 | f2 | Ftot=B*f1 + (1- B)*f2 + 0.005 |  | 
 |  |  |  |  | 0.2 | 0.5 | 0.9
1 | 1.2 | 5 | 1 | (5-6)/(0-6) = 0.167 | 0.339 | 0.589 | 0.922
3 | 0.8 | 2 | (0.8-[-1.3]) /(1.2-[-1.3]) = 0.84 | (2-6)/(0-6) = 0.667 | 0.691 | 0.759 | 0.739
6 | N/A | 0 | 0.5 | 1 | 0.905 | 0.755 | 0.555
7 | -1.3 | 6 | 0 | 0 | 0.005 | 0.005 | 0.005
B named for G.E.P. Box. First to coin the phrase “exploration vs. exploitation”
B = [0 1]

## Slide 19
rule3
rule1
rule6
rule7
Q | 0 | 0.5 | 0.8 | 1
P | 1/500 | 1 | 2 | 500
0.589 | 0.251 | 0.279 | 0.232 | 0.000
0.759 | 0.251 | 0.360 | 0.386 | 0.910
0.755 | 0.251 | 0.358 | 0.382 | 0.090
0.005 | 0.248 | 0.002 | 2E-05 | 0.000
 | Fit. | Pop. | f1 | f2 | Ftot=B*f1 + (1- B)*f2 + 0.005 |  | 
 |  |  |  |  | 0.2 | 0.5 | 0.9
1 | 1.2 | 5 | 1 | (5-6)/(0-6) = 0.167 | 0.339 | 0.589 | 0.922
3 | 0.8 | 2 | (0.8-[-1.3]) /(1.2-[-1.3]) = 0.84 | (2-6)/(0-6) = 0.667 | 0.691 | 0.759 | 0.739
6 | N/A | 0 | 0.5 | 1 | 0.905 | 0.755 | 0.555
7 | -1.3 | 6 | 0 | 0 | 0.005 | 0.005 | 0.005

## Slide 20: Recreate the Cross-Knot
Chart: 
PDF | 0.00018312 | 0.00018312 | 0.0010987 | 0.001648 | 0.0040286 | 0.0073247 | 0.015199 | 0.029116 | 0.090643 | 0.14906 | 0.2679 | 0.12873 | 0.16426 | 0.14063
CDF | 0.00018312 | 0.00036623 | 0.0014649 | 0.003113 | 0.0071415 | 0.014466 | 0.029665 | 0.05878 | 0.14942 | 0.29848 | 0.56638 | 0.69511 | 0.85937 | 1
Go all the way to 15th level of tree (5461 candidates)
Calculate difference from cross-knot
Chart: 

## Slide 21: Results
B** | Q | # OF DESIGNS TO PRESENT | # OF ITERATIONS | Average | St.Dev |  |  |  |  |  | 
0.5 | 0.5 | 3 | 10 | 4.33 | 0.58 | Q | ave. | StDev | experiments | ave. | StDev
0.5 | 0.5 | 4 | 5 | 4.33 | 1.15 | 0.5 | 5.11 | 3.14 | "3-10" | 5.22 | 3.27
0.5 | 0.5 | 5 | 3 | 6.67 | 5.69 | 0.8 | 7.78 | 4.63 | "4-5" | 7.00 | 4.15
0.5 | 0.8 | 3 | 10 | 7.67 | 4.04 | 1 | 7.33 | 4.39 | "5-3" | 8.00 | 4.77
0.5 | 0.8 | 4 | 5 | 9.00 | 5.29 |  |  |  |  |  | 
0.5 | 0.8 | 5 | 3 | 6.67 | 6.11 |  |  |  |  |  | 
0.5 | 1 | 3 | 10 | 3.67 | 3.51 |  |  |  |  |  | 
0.5 | 1 | 4 | 5 | 7.67 | 4.73 |  |  |  |  |  | 
0.5 | 1 | 5 | 3 | 10.67 | 2.31 |  |  |  |  |  | 
After reviewing 30 out of 5461 solutions, we find a solution in 98 percentile.